GROUNDWATER QUALITY MONITORING

Pesticides Survey 2008 - 025905

Date: 	10/09/08

Author : David Evans, Carl Hanson

File : 	WATE/INGW/QUAL/MONI/1

GROUNDWATER QUALITY MONITORING – PESTICIDE survey

## Summary

A survey of pesticides in groundwater was carried out by Environment Canterbury staff during the first three months of 2008.  A total of 97 wells were sampled, located across the region from Kaikoura to the Waitaki River area.  Pesticides were detected in 14 wells.  Most concentrations were very low, but one dieldrin detection was above the MAV.

Overall, the results were comparable to those from the last region-wide pesticide surveys, which were conducted in the mid-1990s. Based on these results, the next region-wide survey of pesticides in groundwater should be conducted in ten years, rather than five years as set out in the proposed NRRP.

## Introduction

Environment Canterbury is required under Section 4.11 (Monitoring the Plan) of the Proposed Natural Resources Regional Plan 2004 (NRRP) to carry out groundwater monitoring for pesticide contamination every 5 years.  The aquifer types outlined in the NRRP are shallow unconfined or semi-confined aquifers that may come under pressure from land use practises such as effluent loading from livestock irrigation, discharges, fertilizer use and waste disposal (NRRP, 2004).

As the criteria in the NRRP for well selection for pesticide sampling is comparable to the criteria used for the selection of Environment Canterbury’s quarterly monitoring program wells, it was decided that these same quarterly wells would be used for the pesticide survey.  The location and depth of these wells give good coverage of the shallow groundwater in Canterbury that is most vulnerable to pesticide contamination.

Therefore, over the period February to April 2008, Environment Canterbury included a screen for pesticides in its quarterly sampling programme. A total of 99 samples were collected from 97 wells (repeat samples were collected from two wells).  The locations of the wells are shown in Figure 1, and the wells are listed in Table 1. The pesticide analyses were done by Hill Laboratories in Hamilton.

## Methodology

Each sample was collected using ECan Groundwater Monitoring procedure EMQ-G002-1, Collection of Groundwater Quality Samples.  The samples were collected from each well in two “Org500” bottles supplied by Hill Laboratories.  These are unpreserved 500ml amber glass jars with a Teflon lined lid.  Each bottle was then labelled with a sample name using either the well number or ECan sample number (this practice of using two different sample names caused some problems and will be discussed later in this report), the date, and time of sample collection.  A Hills field sheet was also filled in and included with the samples.

While in the field, samples were kept cool using a chilly bin and ice packs. At the end of the day, samples from wells north of the Ashburton River (collected by David Evans from ECan’s Christchurch office) were delivered to the Hills Laboratory office in Ferry Road, Christchurch, and then sent via courier to Hill Laboratory in Hamilton for analysis.  Samples from wells south of the Ashburton River (collected by Ross Cressy from ECan’s Timaru office) were stored at approximately 4o C in a refrigerator located at ECan’s Timaru office; these samples were sent in bulk to Hills at the end of each sampling run, typically within 5 days.

## Determinands

The samples were analysed for a suite of 133 pesticides (Tables 2a-2c), including 19 acid herbicides, 25 organochlorine pesticides, and 89 organonitrogen and organophosphorus pesticides. Note that the original quote from Hill Laboratories included triphenylphosphate in the list of determinands, but this compound was not analysed in any of the samples collected.

Tables 2a-2c also shows the detection limits for the determinands analysed. In some cases, the reported detection limit varied those shown in the original quote from Hill Laboratories. The detection limit for all acid herbicides was quoted as 0.00003 g/m3, but the reported detection limits ranged from 0.00004 g/m3 to 0.0001 g/m3. Also, the quoted detection limit for Dichloran was 0.00002 g/m3, but the actual detection limit was 0.000025 g/m3.

In addition, the actual detection limits for some samples differed from those shown in Tables 2a-2c. These differences are highlighted in the notes at the end of Table 1.

## Results

Pesticides were detected in the samples from 14 of the 97 wells sampled (Table 3). In most of these samples, only one pesticide was detected, but two pesticides were detected in the sample from well J40/0343 near Makikihi, and five pesticides were detected in the sample from well K38/0172 at the Ravensdown facility at Seadown. The Makikihi well had not been sampled previously for pesticides.

The Ravensdown well has been sampled repeatedly in the past and has a long history of pesticide detections. The source of the detections in this well is not clear. Smith (1993) reported a plume of groundwater contamination originated at Ravensdown plant. Contaminants in the plume included nitrate, fluoride, and sulphate.  It is not clear whether the pesticides detected in well K38/0172 are related to activities at the plant. Low concentrations of pesticides have been detected in other wells in the Levels Plain area.

Twelve different compounds were detected.  Atrazine and/or atrazine-desethyl were detected in the samples from four wells. Hexachlorobenzene was detected in the samples from three wells in northern Canterbury, and simazine was detected in the samples from two wells.

Only one detection exceeded a Maximum Acceptable Value (MAV) set by the Ministry of Health in 2005 (Table 3). This was a detection of dieldrin in well J40/0343, located near Makikihi, at a concentration of 0.0014 g/m3, compared to the MAV of 0.00004 g/m3. All other detections were well below any MAVs.

Dieldrin was actually detected in samples from two wells near Makikihi. In addition to the sample from well J40/0343, dieldrin was detected at a concentration of 0.0000044 g/m3 in one of two samples from well J40/0042. Neither of these wells is used for drinking-water supply, although J40/0042 has been used for drinking-water supply in the past. Neither of the two Makikihi wells had been sampled for pesticides prior to this survey.

Well J40/0343 is located in an old storage shed, and the well head is recessed slightly below the floor level, such that liquids spilled on the shed floor could easily flow into the well. It is conceivable that the detection in this well was the result of contamination from old chemicals spilled on the shed floor, though it may also indicate soil contamination in the area around the shed, or from a source farther up-gradient.

Well J40/0042 is a large-diameter irrigation well located in a dairy paddock approximately 630 metres south of J40/0343. It also has poor well-head protection, and material from the ground surface can flow directly into the well. It was sampled on two different dates in this survey (2 February 2008 and 17 March 2008), but dieldrin was detected only in the February sample.

## Problems encountered during the survey

Throughout the pesticide survey, a number of complications arose:

- Sample bottles for wells K38/0412 and K37/0358 broke during transit

- For Hills Lab batch 630257, there had to be a repeat analysis meaning that the detection limits where twice what was quoted

- Well L37/0415 was dry so no sample could be collected.  This continued throughout the 3 months the survey was being carried out.

- Triphenylphosphate (SMC) was not analysed for any of the wells as per quote requested

- Well L35/0205 recorded a false positive for organochlorine and had to be resampled.

- The samples sent to Hills were not identified consistently. The samples from south Canterbury were identified by their unique sample No. created from the ECan lab.  The samples from north Canterbury were identified by their well number.  This caused problems as the well number has both letters and numbers and is not unique to any specific sample. In the future, there must be clear, consistent procedures for sample labelling.

- There were major difficulties importing the results into SQUALARC.  In the future, we need to plan for this, and make sure we get the results from the external lab in a format that we can import easily.

## Recommendations

- The next region-wide survey of pesticides in groundwater should be conducted in ten years, rather than five years as set out in the proposed NRRP.

- Wells J40/0343 and J40/0042 should be re-sampled for dieldrin to confirm the detections in this survey. Further investigation of the area may be warranted if the detections are confirmed.

- When receiving large amounts of data from an external laboratory, plans need to be made for how samples will be labelled and how the data will be imported into the ECan database.

Figure 1 Location of Pesticide Sampling Wells

Figure 2 Map showing location of pesticide detections

# Footnotes

Smith, V. R., 1993. Groundwater contamination from activities at a fertiliser works. Environment Canterbury Technical Report R93/37.